## Slide 1
Monitoring, Reporting and Verification
Domenico Gaudioso
28 February 2024
Türkiye: Advancing EU-Türkiye high-level dialogue
on climate action including technical exchanges and trainings on EU ETS
This activity is part of the European Union Climate Dialogues Project (EUCDs)
This publication was funded by the European Union. Its contents are the sole responsibility of the author and do not necessarily reflect the views of the European Union

## Slide 2: Outline
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
What is an MRV system and what is its scope?
MRV in Emission Trading Systems:
  Monitoring
  Reporting
  Verification
MRV issues in the CBAM regulation and implementing legislation

## Slide 3: MRV stands for…
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
The independent auditing of reported emissions data for the purpose of assuring regulators and other stakeholders of its quality
Monitoring
Reporting
Verification
Collecting data on emissions through the direct measurement of releases to the atmosphere or the estimation of emissions based on proxy measurements such as fossil fuel consumption and the carbon content of each fuel
Submitting and documenting emissions data and related information to a governing authority and/or the public
An MRV system should enable users of emissions data to make informed decisions and not have their decisions altered because of false or inaccurate information. An MRV system can be applied to assess the emission profile of an installation, company, city, region or country.

## Slide 4: What is an MRV system?
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
A domestic MRV system directed to monitor both greenhouse gas (GHG) emissions and GHG mitigation actions allows:
Accounting of GHG emissions over time
Publication of Emissions Inventories
Verification of emissions data accuracy
Estimation of the impact/result of planned mitigation actions
Publication of documents that report mitigation efforts in climate change
Verification of mitigation policies’ performance
Support and justification of internal and external policies

## Slide 5: What are the features of a robust MRV system?
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
A robust MRV system should be:
Transparent: The process is open, accessible and clear to various types of audiences. Transparent MRV systems are more credible.
Comparable: The information is comparable over time, between different institutions and different levels of government. Evaluation in comparable MRV systems, allows an evolution and continuous improvement evaluation.
Reliable: The information is accurate. The methodologies are properly applied by skilled and properly trained professionals. The results are verified by independent entities.
Complete: The information covers all required determinants (emission types of interest), installations, emission sources and source streams.
Helpful: The MRV system is linked to the process of public policy formulation.
Integral: The output is channelled to support decision-making of current and future policies.

## Slide 6: MRV in Emission Trading Systems
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
Effective MRV systems for monitoring, reporting, and verification of emissions and other necessary data are at the heart of ensuring the environmental integrity of an ETS.
These systems include, inter alia:
  methodologies for monitoring emissions from regulated entities;
  reporting arrangements for regulated entities;
  verification of reported data (either through independent verifiers or by auditing and self-regulation schemes);
  establishment of registries — systems that record, monitor, and facilitate the creation, trading, and surrender of all allowances within an ETS system;
  approaches to oversee both the primary and secondary allowance markets.

## Slide 7: Elements of a MRV infrastructure
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
MRV rules and procedures:
  Measurement – emissions data
  Reporting – communication of data to relevant stakeholders
  Verification – data review to ensure quality
System architecture:
  reporting system
  trading registry
  trading platform
Institutional structures:
  responsibilities for setting, enforcing and updating MRV tasks allocated to Ministries, departments, agencies
  specified roles for MRV and compliance enforcement
  assigned responsibilities for developing, operating and maintaining system architecture
  coordination/communication among responsible institutions and stakeholders

## Slide 8: MRV approaches by ETS
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
Source: PMR-ICAP, Emissions Trading in Practice: A Handbook on Design and Implementation

## Slide 9: MRV reporting cycle in the EU ETS
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
The annual procedure for monitoring, reporting and verifying (MRV), together with all the associated processes, is known as the ETS compliance cycle.
Industrial installations and aircraft operators (+ maritime operators since 1st January 2024) covered by the EU ETS are required to have an approved monitoring plan for monitoring and reporting annual emissions. This plan is also part of the permit to operate required for industrial installations.
Every year, operators must submit an emissions report. The data for a given year must be verified by an accredited verifier by 31 March of the following year. Once verified, operators must surrender the equivalent number of allowances by 30 April of that year.
The rules related to the compliance cycle are set out in two regulations:
  Monitoring and Reporting Regulation (MRR)
  Accreditation and Verification Regulation (AVR)

## Slide 10: MRV compliance cycle in the EU ETS
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
Source: ECRAN, Workshop Report, 10-11 September 2014, Zagreb, Croatia

## Slide 11: The four phases of the EU ETS 2005-2030
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
Source: ODYSSEE-MURE

## Slide 12
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
 | PHASE I (2005-2007) | PHASE II (2008-2012) | PHASE III (2013-2020) | PHASE IV (2021-2030)
GOAL OF THE PHASE | Pilot the system to demonstrate proof of concept | -8% emissions reduction relative to 1990 levels | -21% emissions reduction relative to 2005 levels | -62% emissions reduction relative to 2005
GEOGRAPHIC SCOPE | EU27 | EU27 Norway Iceland Liechtenstein | EU28 Norway Iceland Liechtenstein | EU28 Norway Iceland Liechtenstein Northern Ireland for electricity generation
GREENHOUSE GASES | Carbon dioxide (CO2) | Same of Phase I plus Nitrous oxide (N2O) via voluntary opt-in by Member States | Same of Phase I plus N2O Perfluorocarbons (PFC) from aluminium production | Same of Phase III
SECTORS | Power generation installations Energy-intensive industries | Same as Phase I plus Aviation in EEA | Phase II plus Aluminium, petro- & other chemicals Carbon capture & storage | Phase iii plus Maritime Buildings/transport Enhancement aviation
CAP | Cap set at national level through NAP Sum of NAP = total EU cap Emissions registered in national registries | -6,5% allowances compared to Phase I Guidance on how to establish NAP Sum of NAP = total EU-wide cap Emissions registered in a EU registry | Single EU-wide cap replaces sum of NAP Linear annual reduction of allowances of -1,74% | Single EU-wide cap replaces sum of NAP Linear annual reduction of allowances of -2,2%
ALLOWANCE MANAGEMENT | Allocation through NAPs Free allocation of nearly all allowances Penalty for non-compliance at €40/t CO2 | Free allocation reduced to 90% of Phase I Free allocation through harmonised NAP Auctioning introduced in some countries Penalty for non-conpliance at €100/t CO2 | Auctioning and free allowance allocation Introduction of a market stability reserve and a new market entrants reserve Introduction of international credits Penalty for non-compliance at €100/t CO2 Increasing with inflation | Strengthened benchmarks and faster phase-out of free allocation Strengthened market stability reserve Establishment of an Innovation Fund for demonstration projects
TRADABLE UNITS | EU Emission Allowances (EUAs) | Same as Phase I plus Certified Emission Reductions (CERs) Emission Reduction Units (ERUs) | Same as Phase II | End of CDM/CERs Introduction of Carbon Border Adjustment Mechanism (CBAM)

## Slide 13: Extension of the EU ETS to new sectors in Phase IV
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
Maritime transport will be included in the ETS from 2024, with a 2-year phase-in period. Large vessels of 5,000 gross tonnage and above must gradually surrender emission allowances (EUA) for an increasing share of their emissions: 40% in 2024, 70% in 2025 and 100% in 2026. The inclusion of smaller vessels and non-CO2-emissions such as CH4 and N2O will likely start from 2026 onwards.
The Commission will assess a possible extension to municipal waste incineration from 2028.
As part of the 2023 revisions of the ETS Directive, a new emissions trading system named ETS 2 has been created, separate from the existing EU ETS. This new system will start in 2027; it will cover and address the CO2 emissions from fuel combustion in buildings, road transport and additional sectors (mainly small industry not covered by the existing EU ETS).

## Slide 14: Monitoring emissions
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
Monitoring refers to the process of collecting the data necessary to quantify emissions.
The ETS regulator should define the specific monitoring requirements for all emission sources included in the scope of the system.
Monitoring guidelines must be available for each sector covered by the ETS.

## Slide 15: Content of a monitoring plan
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
The EU ETS requires installations to have a monitoring plan. This plan outlines the steps the installation will take to monitor its emissions, including the site- or company-specific methodologies for measuring, calculating, and reporting data, and are subject to approval by the regulatory authority.
The monitoring plan of an installation usually includes factors such as the following;
In the EU, each installation is classified within three categories according to the annual volume of emissions. The source streams can be classified as: minor source, de-minimis or major source streams.
General information
Categorisation
description of activities to be monitored, list of emissions sources and source streams;
description of procedures for assigning monitoring and reporting responsibilities, for managing responsible personnel;
description of the procedure for regular evaluation of the monitoring plan’s appropriateness.

## Slide 16: Monitoring in an ETS Calculation vs. Measurement
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
Here are the differences between the calculation and the measurement approaches:

## Slide 17: Monitoring in an ETS – Calculation approach
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
The typical estimation methodology for GHG emissions is based on multiplying activity data by an emission factor. Some methods also include an oxidation factor (for combustion emissions) or a conversion factor (for process emissions).
Source: http://ec.europa.eu/clima/policies/ets/monitoring/docs /gd1_guidance_installations_en.pdf
Note: The oxidation factor and conversion factor are used to correct the emission numbers in case of incomplete chemical reactions

## Slide 18: Monitoring emissions in the EU ETS
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
In the EU ETS, the aim is to balance data quality and costs
Use as far as possible available data and existing equipment
Therefore the Monitoring and Reporting Regulation (MRR) provide for a building block system:
  Options for overall approach
  Options for each parameter (fuel consumption, emission factors,...)
  Different tiers (=precision levels) possible
For bigger emissions higher data quality is required
CO2 resulting from use or combustion of biomass (including bioliquids and biofuels) is generally considered to be rated as zero (i.e. Emission Factor = 0). Thus, no allowances for emissions stemming from biomass have to be surrendered, and the associated costs are avoided.

## Slide 19: Use of default values for calculation factors
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
In order to avoid excessive costs, the Monitoring and Reporting Regulation (MRR) allows for the use of default values for calculation factors (in particular emission factors), based on:
authoritative scientific literature (e.g. IPCC reports);
standard factors used by the Member State for its national inventory;
other values agreed with the national competent authority.

## Slide 20: Reporting emissions
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
Regulated entities need to report their monitoring data to the regulator in a standardized and transparent form.
Emissions report timing should be aligned with compliance time frames, typically providing sufficient time after the end of the monitoring period for reports to be prepared.

## Slide 21: Designing an efficient reporting process
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
The regulator can design an efficient reporting process by:
providing regulated entities with clear guidance about reporting requirements, including:
  the type of information to report;
  the frequency of reporting, and
  how long records should be kept (typically between 3 and 10 years);
standardizing emissions reports to ensure consistency over time and across reporters;
aligning timing of emissions reports with existing financial reporting cycles and compliance time frames; and
creating electronic reporting formats to cut down on processing time and transcription errors, for example, through web-based reporting platforms that can reduce time demands, easily manage large volumes of data, automatically check for errors, and bolster security.

## Slide 22: Reporting emissions in the EU ETS
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
According to the MRR regulation, emission reports shall include:
information needed to identify the emission source;
reference to its latest approved monitoring plan;
information on possible changes in the operations of the installation (or aircraft);
description of the methodology used to estimate emissions (including activity data, emission factors and other coefficients, in case of calculations)
The Commission has provided a template for the verification report, its use by Member States is voluntary

## Slide 23: Verifying emission reports
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
The objective of verification is to create trust in the data submitted by operators. A key decision for policy makers to make is the type of verifier that will do the verification. Different options can be distinguished:
Verification by the regulator: the regulator responsible for implementing the emission trading system verifies the data report and checks compliance with the system specific requirements;
Verification by an independent expert hired by the regulator: institutes or experts are hired through consultancy projects, procurement services, or nominated as preferred experts by the regulator and carry out verification activities on behalf of the regulator;
Verification by an approved third- party verifier: an organisation that is independent from the regulator and other parties (that is, the organisation does the verification and takes responsibility for the conclusions and the decision to issue a verification report);
Verification by an approved individual independent auditor: an individual person instead of an organisation (that is, the individual takes responsibility for the conclusions and the decision to issue an opinion statement).

## Slide 24: Criteria to choose among verification schemes
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
The type of verifier model can evolve over time.
In the early years or a pilot phase, it could be that policy makers choose to select option 1 or 2 in order to have more control over the verification system and to build up sufficient competent verifier resources.
Over time an ET system usually evolves toward option 3 which is the most common model applied in the EU ETS and other existing ET schemes.
Most ET systems use option 3 from the start as they want to align with other schemes, link, or choose to apply recognised international standards.

## Slide 25: Verification process
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
The aim of the verification process is to independently assess, whether:
monitoring has been carried out in compliance with the approved monitoring plan;
the compilation of the report is in line with the requirements of the MRR;
the emission report does not contain any misstatements with regards to the emission data contained and;
there is potential for improvement in the operator’s performance (for more information see Art. 30 of the AVR).

## Slide 26: Verifying emission reports in the EU ETS
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
The EU ETS requires operators of installations or aviation operators under the system to submit annual emissions reports which are verified by an independent verifier, in accordance with the Accreditation and Verification Regulation (AVR).
The AVR sets out detailed requirements for the accreditation of the verifiers and the preparation and implementation of the verification. It is complemented by an extensive set of detailed guidance. This allows for strongly harmonised approaches in the EU Member States, increasing trust in the ETS.
This high level of harmonisation has been developed based on a situation with virtually no harmonisation and a very basic set of rules, using assessments and information exchange between EU Member States to identify potential for improvements and good practices.

## Slide 27: Accreditation of verifiers
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
A verifier can be a legal entity or legal person accredited by a national accreditation body (NAB) or a natural person that is certified by a National Certification Authority (NCA) in compliance with the requirements of the AVR. Accreditation under the EU ETS is based on Regulation (EC) No 2067/2018.
NAB reviews the information provided by the applicant and ensures that he has processes in place which comply with the AVR requirements and is able to perform the verification process.
The NAB has to continuously ensure the quality of the verification process, through annual visits and periodic reassessments.
For the sake of quality, the AVR also requires that the competence and performance of the NAB is monitored by the EU Member State that has appointed the NAB (see Art 65 of the AVR). In addition, a regular and independent peer evaluation is organised by the European Cooperation for Accreditation (EA).

## Slide 28: Carbon Border Adjustment Mechanism (CBAM)
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
CBAM addresses the risk of carbon leakage, which occurs when industries transfer polluting production to other countries with less stringent climate policies, or when EU products are replaced by more carbon-intensive imports.
Carbon leakage can shift emissions outside of Europe and seriously undermine EU and global climate efforts.
That’s why the EU has introduced a new – green - mechanism for imports of goods from outside the EU: a system that puts a fair price on the carbon emitted during production, and that encourages cleaner industry in non-EU countries.

## Slide 29: How will the CBAM work?
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
EU importers of goods covered by the CBAM will need to buy CBAM certificates. The price of the certificates will be calculated depending on the weekly average auction price of EU ETS allowances expressed in € / tonne of CO2 emitted.
EU importers of goods covered by the CBAM will need to buy CBAM certificates. The price of the certificates will be calculated depending on the weekly average auction price of EU ETS allowances expressed in € / tonne of CO2 emitted.
The EU importer must declare by 31 May each year the quantity of goods and the embedded emissions in those goods imported into the EU in the preceding year. At the same time, the importer surrenders the number of CBAM certificates that corresponds to the amount of greenhouse gas emissions embedded in the products.
If importers can prove, based on verified information from third country producers, that a carbon price has already been paid during the production of the imported goods, the corresponding amount can be deducted from their final bill.
The EU importer must declare by 31 May each year the quantity of goods and the embedded emissions (CO2, N2O and PFCs) in those goods imported into the EU in the preceding year. At the same time, the importer surrenders the number of CBAM certificates that corresponds to the amount of greenhouse gas emissions embedded in the products.
If importers can prove, based on verified information from third country producers, that a carbon price has already been paid during the production of the imported goods, the corresponding amount can be deducted from their final bill.

## Slide 30: Covered goods
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
The CBAM will initially apply to imports of the goods listed in Annex I (iron and steel, cement, aluminium, fertilisers and electricity).
These sectors have been selected following specific criteria in particular, due to their high risk of carbon leakage and high carbon emissions which will eventually – once fully phased in – capture more than 50% of the emissions of the ETS covered sectors.
Annex II lists goods (specific CN codes) for which only direct emissions are to be taken into account

## Slide 31: What are embedded emissions?
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
The EU ETS requires operators to pay a price for their own (“direct”) emissions. However, if they consume electricity, they also experience the CO2 costs included in the price of electricity they purchase (“indirect emissions”). The same applies to the input materials needed for their production process, and which may be supplied by an EU ETS installation. These so-called precursors therefore contribute to the CO2 costs the EU ETS installation faces.
The “embedded emissions” are defined in parallel to the emissions causing CO2 costs in the EU ETS: they take into account the direct and indirect emissions of the production process as well as the embedded emissions of precursors. They are similar in concept to a carbon footprint of the goods.

## Slide 32: Scopes in product footprints vs. CBAM
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 

## Slide 33: Governance of CBAM
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 

## Slide 34: CBAM declaration
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
The CBAM declaration shall contain the following information:
Total quantity of each type of goods imported during the preceding year (mWh for electricity and in tonnes for other goods);
The total embedded emissions in the goods (tonnes CO2 emissions/mWh for electricity or, for other goods, tonnes of CO2 emissions/tonne of each good);
The total number of CBAM certificates to be surrendered;
Copies of verification reports, issued by accredited verifiers.

## Slide 35: CBAM reporting regulation (1)
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
On 17 August, the EU has published its Carbon Border Adjustment Mechanism (CBAM) reporting regulation for 2023-2025.
This regulation governs how companies should report emissions from imported materials in the transitional period from 1 October 2023 to the 31 December 2025.
Until the full implementation starts (1st January 2026), there will be no cost of compliance.
“Embedded emissions” in shipments of imported materials will be monitored. Failure to comply will result in penalties of €10-€50 per tonne or higher.
Globally imported goods will be regulated more closely due to new rules from the European Union.

## Slide 36: CBAM reporting regulation (2)
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
From October, importers in Europe will be required to report key details every quarter: including all “embedded emissions” in shipments of iron and steel, cement, aluminium, fertilisers, electricity, and hydrogen.
Details will include the quantity of goods imported, their geographical source – including the installation at which they were produced – the method of production, and their specific embedded emissions.
A CBAM Transitional Registry will enable information exchange in the transiional period.
While importers are asked to collect fourth quarter data as of 1 October 2023, their first report has to be submitted by 31 January 2024.

## Slide 37: Calculation of emissions
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
The draft implementing regulation provides some flexibility on the values used to calculate embedded emissions at the point of importation. During the first year of implementation, companies will have the choice of reporting embedded emissions in three different ways:
full reporting under the new methodology (EU methodology: Annex IV, CBAM Regulation, which is broadly in line with the EU Emissions Trading Scheme);
reporting based on equivalent third-country (non-EU) national systems; and
reporting based on default reference values.

## Slide 38: Default values for the transitional period
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
On 22 December 2023 the European Commission has published default values to calculate direct and indirect emissions from iron and steel, cement, fertilisers, aluminium and hydrogen, when the declarants do not have or are not able to report actual emissions.
The general approach for determining embedded direct emissions for electricity as CBAM good is to use default values for the CO2 emission factors, which represent the average emission factors of the electricity produced from fossil fuels in the country of origin, based on data from the International Energy Agency (IEA).

## Slide 39: Verification of embedded emissions
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
Declared embedded emissions must be verified by an independent, accredited verifier, according to articles 8(1) and 18(1).
Any person accredited in accordance with regulation (EU) 2018/2067 (implementing regulation on the verification of data) for a relevant group of activities shall be an accredited CBAM verifier.
A national accreditation body may, on request, accredit a person to be a verifier for the purpose of this Regulation where it considers, on the basis of the documentation submitted to it, that such person has the capacity to apply the verification principles referred to in Annex VI.

## Slide 40: What are the immediate tasks for companies?
<title of the slide>
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project | 
Identify which of your imports are subject to CBAM regulations. Engage with suppliers and manufacturers to gather emissions data for imported goods. Collect information on carbon pricing schemes in countries of origin for your CBAM goods.
Get registered as a CBAM declarant or have your indirect customs representative registered.
Get access to the transitional CBAM registry. This is the interface for regulators and regulated entities for the transitional period.
Learn how to handle the CBAM reporting template published by the EU.
Establish processes to collect emissions data and set aside personnel capacities to handle CBAM duties.
Make use of EU ETS allowance price forecast and embedded carbon projections to assess the medium-term economic implications of CBAM regulations on your supply chain and business.
Understand the implications of CBAM on your supply chain and assess your price and regulatory risk in different countries.

## Slide 41: Thanks for your attention!
Türkiye: Advancing EU-Türkiye high-level dialogue on climate action including technical exchanges and trainings on EU ETS - An “EU Climate Dialogues (EUCD)” Project8 |